## Slide 1
Big Data tools for monitoring the impact of
IWMP-MGNREGS projects under DISHA Dashboard
Presented by,
Shivanand Nalgire (193350009)
Centre for Technology Alternatives for Rural Areas
Indian Institute of Technology Bombay
Guided by,
Prof. Pennan Chinnasamy
Master’s Thesis Project-2 Mid-progress Presentation
Examiners
Prof. N.C. Narayanan Prof. Satish B. Agnihotri

## Slide 2: Content
Introduction
  Objectives
  Project timeline
Model development
  Land Surface Ecological status and monitoring
  RS based Land Surface Ecological Indicators
Temporal analysis
Weight generation methods
Principal Component Analysis
Model summary
Results and discussions

## Slide 3: Introduction
Illustrative image for RS data analysis Source: (Belgiu and Csillik., 2018)
DISHA Dashboard – System for M&E of schemes
Enables data driven governance of 43 schemes
Monitor impacts of IWMP-MGNREGS projects
Index based M&E framework
Open source remote sensing data
Introduction
Model development
RS Data analysis
Model summary
Results and discussions

## Slide 4: Objectives
To develop an index based multidimensional M&E framework for assessing the impact of IWMP-MGNREGS projects
To analyze the data using M&E framework and validate the model using secondary data
To develop a web application for automated near-real time monitoring and reporting of the impact of IWMP-MGNREGS projects
Introduction
Model development
RS Data analysis
Model summary
Results and discussions

## Slide 5: Project timeline and progress
Jan
2021
Dec
2020
Mapping & Data Analysis using model
Secondary data analysis &
model validation
M&E of IWMP using RSEI
Web Dashboard & Documentation
Model update
Oct-Nov 2020
Developing remote sensing data pipeline
Secondary data analysis for model validation
M&E of IWMP projects
Dashboard design
Weightage of indices
Analyzing data using developed model
Model improvement
Scaling model at Maharashtra level
Protocol for using the M&E framework
Model update
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
February
2021
March- April
2021

## Slide 6: Ecological status and monitoring
IWMP-NRM:
  Enhance soil moisture regime
  Regenerate natural vegetation
  Increase productive land, production and productivity
Termed as Ecological Status of Land Surfaces (Kennedy et al., 2009; Xu et al., 2019)
Assessed by Ecological Monitoring of Land Surfaces (Willis, 2015)
Using Land Surface Ecological Indicators (Jones et al., 2009)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions

## Slide 7: Land Surface Ecological Indicators
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Indicators derived from System Dynamics framework – ‘Pressure State Response’ framework (Friend and Rapport., 1979) based on notion of causality (Hughey et al., 2004)
Ecological changes  significant alteration in characteristics of land surfaces (Willis, 2015)
Ecological indicators of these characteristics are – Moisture, Greenness, Dryness, Heat (Xu et al., 2019)
IWMP-MGNREGS Projects
Ecological status
Change in production, crop area

## Slide 8: RS based Land Surface Ecological Indicators
Any ecological changes will have a significant alteration in important characteristics of land surfaces. (Willis, 2015; Xu et al., 2019)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Notion

## Slide 9: Weight generation for composite index
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Sr. No. | Types of index weight determination methods | Method | Remark | Citation for remark
1 | Subjective methods | AHP / Delphi | 1) Subjective judgement may affect weight distribution in practice 2) Limited by large sample size 3) Less scalable and resilient | 1) (Xu et al., 2018) 2) (Liao and Jiang, 2020)
2 | Objective methods | PCA | 1) Superior for evaluation of multidimensional indexes 2) Resilient against the impact of co-linearity 3) Automatic and objective weight allocation 4) More scalable | 1) (Xu et al., 2019) 2) (Hu and Xu, 2019) 3) (Gau and Zhao, 2020) 4) (Xu et al., 2018) 5) (Liao and Jiang, 2020) 6) (Hu and Xu, 2018)

## Slide 10: Worldwide practices of RSEI
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Sr. No. | Paper | Authors | RSEI Indices used | Aggregation/weighing technique
1 | Detecting Ecological Changes with a Remote Sensing Based Ecological Index (RSEI) Produced Time Series and Change Vector Analysis | (Xu et al., 2019) | NDVI, IBI | Principal Component Analysis (PCA)
2 | A new remote sensing index for assessing the spatial heterogeneity in urban ecological quality: A case from Fuzhou City, China | (Hu and Xu, 2018) | NDVI, NDBSI, LSM, LST,IBI, SI | Principal Component Analysis (PCA)
3 | A new remote sensing index based on the pressure-state-response framework to assess regional ecological change | (Hu and Xu, 2019) | NDBSI, NDVI | Principal Component Analysis (PCA)
4 | Eco-Environmental Quality Monitoring in Beijing, China, Using an RSEI-Based Approach Combined With Random Forest Algorithms | (Gou and Zhao, 2020) | NDVI; NDBSI; LST | Principal Component Analysis (PCA)
5 | A remote sensing index for assessment of regional ecological changes. | (HanQiu, 2013) | - | Principal Component Analysis (PCA)
6 | Prediction of ecological effects of potential population and impervious surface increases using a remote sensing based ecological index (RSEI) | (Xu et al., 2018) | NDVI, LST, NDSI | Principal Component Analysis (PCA)
7 | Evaluation of the Spatiotemporal Variations in the Eco-environmental Quality in China Based on the Remote Sensing Ecological Index | (Liao and Jiang, 2020) | NDVI, NDBI, NDWI | Delphi Method, AHP, PCA

## Slide 11: Study Area
242 out of 1,344 IWMP watersheds i.e. highest are in Maharashtra
Latur district as pilot project
Model validation with secondary data

## Slide 12
Latur district NDVI 2000
Latur district NDVI 2005
Latur district NDVI 2010
Latur district NDVI 2014

## Slide 13: Temporal NDVI (2000-14)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
<0: Water
0.1: Bare land
> 0.1: Vegetation
Rouse, (1974)

## Slide 14: Temporal NDMI (2000-14)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
<0.2 : Extra dry
0.2 – 0.4: Dry
0.4 – 0.6 : Wet
>0.6 : Extreme wet
Wang and Qu, (2007)

## Slide 15: Temporal NDWI (2000-14)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
<0 : Drought conditions
>0 : Vegetation and soil moisture content
Gao, (1996)

## Slide 16: Temporal NDDI (2000-14)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
>0.5 : Extreme drought
0.3-0.5: Moderate drought
0.2-0.3 : Mild drought
-1 to 0.2 : No drought
Gu et al., (2007)

## Slide 17: Temporal SIWSI (2000-14)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
>0 : Canopy water stress
Ceccato et al., (2001)

## Slide 18: Preliminary Principal Component Analysis (5 Indices)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Uncorrelated variables
Principle components

## Slide 19: Preliminary RSEI Calculation (5 Indices)
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
RSEI5 = 1 – (PC1 + PC2 + PC3)
Normalizing the weights
Higher the RSEI5, better the ecological status of a region

## Slide 20: Comparative analysis of RSEI5
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Sr. No. | Index | R-square
1 | NDVI | 83.35%
2 | NDWI | 76.29%
3 | NDMI | 62%
4 | NDDI | 74%
5 | SIWSI | 74.34%
6 | RSEI5 | 87.22%
Regression analysis
  Area under crop in Latur district from 2000-14
  Remote sensing indices - Landsat-7 ETM+
RSEI5 shows strong positive correlation of 0.934 with area under crop

## Slide 21: Comparative analysis of RSEI5
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Sr. No. | Index | R-square
1 | NDVI | 63.00%
2 | NDWI | 54%
3 | NDMI | 60.10%
4 | NDDI | 47%
5 | SIWSI | 52%
6 | RSEI5 | 66.25%
Regression analysis
  Crop production in Latur district from 2000-14
  Remote sensing indices - Landsat-7 ETM+
Newly developed RSEI5 shows a strong positive correlation of 0.814 with crop production

## Slide 22: Results and discussion
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Preliminary RSEI5 shows strong positive correlation with crop area and production (0.934 and 0.814 res.)
RSEI accounts for holistic representation of land surface ecological status
Beta version (5 indices)
Full model with 22 indices (ongoing)

## Slide 23: Future work
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Feb 2021
Jan
2021
Dec
2020
Mapping & Data Analysis using model
Secondary data analysis &
model validation
M&E of IWMP using RSEI
Web dashboard & Documentation
Model update
Oct-Nov 2020
Developing remote sensing data pipeline
Secondary data analysis for model validation
M&E of IWMP projects
Dashboard design
Weightage of indices
Analyzing data using developed model
Model improvement
Scaling model at Maharashtra level
Protocol for using the M&E framework
Model update
Mar-Apr
2021
Non Performing Areas

## Slide 24: References
Behling, R., Bochow, M., Foerster, S., Roessner, S. and Kaufmann, H., 2015. Automated GIS-based derivation of urban ecological indicators using hyperspectral remote sensing and height information. Ecological Indicators, 48, pp.218-234.
Belgiu, M. and Csillik, O., 2018. Sentinel-2 cropland mapping using pixel-based and object-based time-weighted dynamic time warping analysis. Remote sensing of environment, 204, pp.509-523.
Ceccato, P., Flasse, S., Tarantola, S., Jacquemoud, S. and Grégoire, J.M., 2001. Detecting vegetation leaf water content using reflectance in the optical domain. Remote sensing of environment, 77(1), pp.22-33.
Friend, A. and Rapport D., 1979. Towards a comprehensive framework for environmental statistics: a stress-response approach. Statistics Canada 11-510, Ottawa, 1979.
Gao, B.C., 1996. NDWI—A normalized difference water index for remote sensing of vegetation liquid water from space. Remote sensing of environment, 58(3), pp.257-266.
Gou, R. and Zhao, J., 2020. Eco-Environmental Quality Monitoring in Beijing, China, Using an RSEI-Based Approach Combined With Random Forest Algorithms. IEEE Access, 8, pp.196657-196666.
Gu, Y., Brown, J.F., Verdin, J.P. and Wardlow, B., 2007. A five‐year analysis of MODIS NDVI and NDWI for grassland drought assessment over the central Great Plains of the United States. Geophysical research letters, 34(6), pp.1-6.
Hughey, K.F., Cullen, R., Kerr, G.N. and Cook, A.J., 2004. Application of the pressure–state–response framework to perceptions reporting of the state of the New Zealand environment. Journal of Environmental Management, 70(1), pp.85-93.
Hu, X., Hong, W., Qiu, R., Hong, T., Chen, C. and Wu, C., 2015. Geographic variations of ecosystem service intensity in Fuzhou City, China. Science of The Total Environment, 512, pp.215-226.
Jones, D.A., Hansen, A.J., Bly, K., Doherty, K., Verschuyl, J.P., Paugh, J.I., Carle, R. and Story, S.J., 2009. Monitoring land use and cover around parks: A conceptual approach. Remote sensing of environment, 113(7), pp.1346-1356.
Kennedy, R.E., Townsend, P.A., Gross, J.E., Cohen, W.B., Bolstad, P., Wang, Y.Q. and Adams, P., 2009. Remote sensing change detection tools for natural resource managers: Understanding concepts and tradeoffs in the design of landscape monitoring projects. Remote sensing of environment, 113(7), pp.1382-1396.
Liao, W. and Jiang, W., 2020. Evaluation of the Spatiotemporal Variations in the Eco-environmental Quality in China Based on the Remote Sensing Ecological Index. Remote Sensing, 12(15), p.2462.
Nguyen, M.D., Baez-Villanueva, O.M., Bui, D.D., Nguyen, P.T. and Ribbe, L., 2020. Harmonization of Landsat and Sentinel 2 for Crop Monitoring in Drought Prone Areas: Case Studies of Ninh Thuan (Vietnam) and Bekaa (Lebanon). Remote Sensing, 12(2), p.281.
Wang, L. and Qu, J.J., 2007. NMDI: A normalized multi‐band drought index for monitoring soil and vegetation moisture with satellite remote sensing. Geophysical Research Letters, 34(20), pp.1-5.
Willis, K.S., 2015. Remote sensing change detection for ecological monitoring in United States protected areas. Biological Conservation, 182, pp.233-242.
Xu, H., 2013. A remote sensing index for assessment of regional ecological changes. China Environmental Science, 33(5), pp.889-897.
Xu, H., Wang, M., Shi, T., Guan, H., Fang, C. and Lin, Z., 2018. Prediction of ecological effects of potential population and impervious surface increases using a remote sensing based ecological index (RSEI). Ecological indicators, 93, pp.730-740.
Xu, H., Wang, Y., Guan, H., Shi, T. and Hu, X., 2019. Detecting Ecological Changes with a Remote Sensing Based Ecological Index (RSEI) Produced Time Series and Change Vector Analysis. Remote Sensing, 11(20), p.2345.

## Slide 25: Softwares / tools used
Google Earth Engine
  Python API
  JavaScript API
Python for Data Analysis

## Slide 26
Thank you !!!

## Slide 27: PSR Framework

## Slide 28: Crops in Latur
Sr. No. | Season | Crop
1 | Khariff | Bajra, Cotton, Jowar, Groundnut, Maize, Green gram, Soybean, Sunflower
2 | Rabi | Wheat, Urad, Gram, Linseed, Mustard
3 | Summer | Sunflower, Groundnut
4 | Whole year | Sugarcane

## Slide 29: Mann Kendall test
Introduction
Model development
RS Data analysis
Model summary
Results and discussions
Mann-Kendall Trend Test (MK test) is used to analyze time series data
    H0: There is no trend in data
    H1: There is trend in the (Upward or downward)
pyMannKendall 1.4.1 library in Python
Increasing trend (with p-value: 0.00153)

## Slide 30: Illustrative prototype
Need to see district wise statistics
But here one glance view
No need to see 36 districts and taluks reports
Spatial idea of where does a shoe pinch
No need to wait till the annual report arrives but near real time
Plan for immediate intervention

## Slide 31
Latur district NDVI 2000
Latur district NDVI 2001
Latur district NDVI 2002
Latur district NDVI 2003
Latur district NDVI 2004
Latur district NDVI 2005
Latur district NDVI 2006
Latur district NDVI 2003

## Slide 32
Latur district NDVI 2007
Latur district NDVI 2008
Latur district NDVI 2009
Latur district NDVI 2010
Latur district NDVI 2011
Latur district NDVI 2012
Latur district NDVI 2013
Latur district NDVI 2014

## Slide 33
EIGENVALUES:
  The eigenvalue is a measure of how much of the variance of the observed variables a factor explains.

## Slide 34
Chart: Year
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
precipitation | 997.68 | 831.46 | 730.37 | 684.19 | 669.62 | 1195.97 | 1154.98 | 1086.99 | 871.64 | 873.96 | 1245.25 | 893.02 | 883.58 | 1042.59 | 753.69
Conversions of agricultural lands
Total agricultural land vs area under cultivation
How much fallow land changed to cultivation